### Journal of the Acoustical Society of America

### Journal Description

Since 1929 The Journal of the Acoustical Society of America has been the leading source of theoretical and experimental research results in the broad interdisciplinary subject of sound. The Journal serves physical scientists, life scientists, engineers, psychologists, physiologists, architects, musicians, and speech communication specialists.

Subject coverage includes: linear and nonlinear acoustics; aeroacoustics, underwater sound and acoustical oceanography; ultrasonics and quantum acoustics; architectural and structural acoustics and vibration; speech, music and noise; psychology and physiology of hearing; engineering acoustics, sound transducers and measurements; bioacoustics, animal bioacoustics and bioresponse to vibration.

All submissions for publication are subject to peer review to determine their suitability for publication.

In addition to contributed papers, the Journal contains news items of interest to acoustical scientists, book reviews, references to contemporary papers in acoustics, reviews of acoustical patents, and news on the development of standards. Periodically the Journal also issues cumulative indexes of published articles.

## Low-frequency noise from large wind turbines

J. Acoust. Soc. Am. Volume 129, Issue 6, pp. 3727-3744 (2011); (18 pages)

Henrik Møller and Christian Sejer Pedersen

Section of Acoustics, Aalborg University, Fredrik Bajers Vej 7-B5, DK-9220 Aalborg Ø, Denmark

As wind turbines get larger, worries have emerged that the turbine noise would move down in frequency and that the low-frequency noise would cause annoyance for the neighbors. The noise emission from 48 wind turbines with nominal electric power up to 3.6 MW is analyzed and discussed. The relative amount of low-frequency noise is higher for large turbines (2.3–3.6 MW) than for small turbines (≤ 2 MW), and the difference is statistically significant. The difference can also be expressed as a downward shift of the spectrum of approximately one-third of an octave. A further shift of similar size is suggested for future turbines in the 10-MW range. Due to the air absorption, the higher low-frequency content becomes even more pronounced, when sound pressure levels in relevant neighbor distances are considered. Even when A-weighted levels are considered, a substantial part of the noise is at low frequencies, and for several of the investigated large turbines, the one-third-octave band with the highest level is at or below 250 Hz. It is thus beyond any doubt that the low-frequency part of the spectrum plays an important role in the noise at the neighbors.

© 2011 Acoustical Society of America

## ACKNOWLEDGMENTS

The measurements were carried out by Delta. Financial support was obtained from the Energy Research Programme under the Danish Energy Agency, and from Aalborg University.